## Slide 1
Syed Samar Abbas
Mechanical Power Transmission
MMET 301

## Slide 2
Failures in MPT
Mechanical power transmission systems can experience several types of failures due to design, manufacturing, installation, or operational issues.
Let’s review it by components!
We have had the following mechanisms covered:
  Brakes and Clutches
  Belt drives
  Chains and sprockets
  Gears
  Couplings (and universal)
  Bearings

## Slide 3
Failures of Brakes
1. Hydraulic Issues:
- Brake Fluid Leak:
A leak in the hydraulic system reduces brake pressure, making it difficult or impossible to stop the vehicle.
- Air in the Brake Lines:
Air pockets in the brake lines can form due to cavitation, leading to reduced braking effectiveness.
- Low Brake Fluid Levels:
Insufficient brake fluid prevents proper hydraulic pressure from being applied.
2. Overheating:
- Brake Fade:
Prolonged or excessive braking (e.g., driving downhill for long periods).
- Glazed Brake Pads or Rotors:
Overheating can cause the brake pads or rotors to develop a smooth, glass-like surface, reducing their ability to generate friction.

## Slide 4
Failures of Brakes
3. Mechanical Failures:
- Worn Brake Pads or Shoes:
Excessively worn pads or shoes can reduce braking performance.
- Damaged Brake Rotors or Drums:
Damaged rotors and drums can cause uneven braking or reduce braking efficiency.
- Faulty Calipers:
Calipers that fail to engage or release properly can reduce braking force or cause the brakes to stick.
4. Lubrication-related failures:
- While some parts may require lubrication (for instance: Brake Caliper Pins/Slides, or in drum brakes, contact points where the brake shoes touch the backing plate), others should essentially remain free of contamination (as an example: pads and rotors or general friction surfaces).
- Do you think brake shoes should be lubricated?

## Slide 5
Failures of Clutches
1. Clutch Slipping:
The clutch does not fully engage, resulting in a loss of power transmission.
Causes could be:
- Worn Clutch Disc: Excessive wear reduces the friction material on the disc.
- Oil or Grease Contamination: Leakage from the engine or transmission can contaminate the friction surfaces.
- Weak Pressure Plate Springs: Insufficient clamping force leads to slippage.
- Incorrect Adjustment: Improper free play in the clutch pedal can cause incomplete engagement.
2. Clutch Dragging:
The clutch does not fully disengage, making gear shifting difficult and causing grinding noises.
Causes could be:
- Improper Adjustment: Insufficient clearance in the clutch linkage or cable.
-Warped Clutch Disc or Flywheel: Deformation prevents smooth disengagement.

## Slide 6
Failures of Clutches
3. Clutch Chatter
A jerky or shuddering engagement of the clutch, especially when starting from a stop.
Causes could be:
- Contaminated Friction Surfaces: Oil, grease, or dirt on the clutch disc or flywheel.
- Warped or Glazed Components: Excessive heat causes glazing or warping of the clutch disc or flywheel.
- Weak Engine Mounts: Loose or damaged mounts allow excessive vibration.
4. Can you think of a failure mechanism related to clutch actuation?
5. Does the rule of not lubricating the friction surfaces apply?

## Slide 7
Failures of Belt drives
1. Belt Slippage
The belt slips over the pulley, causing a loss of power transmission.
Causes:
- Insufficient Tension: Improperly tensioned belts fail to maintain frictional contact.
- Worn Pulley Surfaces: Reduced grip due to wear or polishing of pulley surfaces.
- Oil or Grease Contamination: Reduces the friction needed for power transmission.
2. Belt Breakage
The belt snaps or breaks under operation.
Causes:
- Overloading: Excessive force on the belt beyond its tensile strength.
- Misalignment: Misaligned pulleys create uneven stress on the belt.
- Aging: Natural degradation of the belt material over time.

## Slide 8
Failures of Belt drives
3. Pulley-Related Failures
Pulleys fail to operate properly, leading to belt damage.
Causes:
- Worn Pulley Grooves: Smooth or uneven grooves reduce grip.
- Damaged Pulley Surface: Physical damage can cause uneven wear or belt damage.
- Improper Pulley Size: Incorrect pulley size can strain the belt.
- Proper lubrication: is essential for ensuring smooth operation, reducing wear, and extending the life of the system. However, over-lubrication or lubricating the wrong areas can cause problems, such as belt slippage.
- Belt Contact Surfaces: The grooves or flat surfaces of the pulley where the belt runs must remain free of lubricant.

## Slide 9
Failures of Chains, sprockets and
Gears
Wear-related failures:
  - Sprocket Tooth Wear:
  Continuous interaction with the chain leads to gradual material loss on the sprocket teeth.
  Caused by improper lubrication, abrasive contaminants, or excessive loading.
  - Chain Link Wear:
  Pins, rollers, and bushings of the chain wear out due to friction.
  Poor lubrication or alignment issues exacerbate this problem.
  - Adhesive Wear of gears:
  Caused by metal-to-metal contact due to inadequate lubrication.
  Results in material transfer between gear teeth.
  - Abrasive Wear of gears:
  Occurs when hard particles in the lubricant or environment cause material loss.
  Common in contaminated environments.

## Slide 10
Failures of Chains, sprockets and
Gears
2. Fatigue-related failures:
  - Chain Fatigue:
  Repeated cyclic loading can cause fatigue cracks in the chain's plates or links.
  Occurs due to improper tension or high cyclic stress.
  - Sprocket Fatigue:
  High stress concentrations on sprocket teeth can lead to crack initiation and propagation.
  - Tooth Bending Fatigue:
  High cyclic stresses at the gear tooth roots cause cracks that propagate and eventually lead to tooth breakage.
  Occurs due to excessive loading or poor design.
  - Surface Fatigue (Contact Fatigue):
  Micro-cracks develop on the gear surface due to repeated stress cycles, leading to spalling or material flaking.

## Slide 11
Failure Monitoring
Design Stage:
  Allowable stresses.
  Flow field analysis (for the case of lubricants).
  Heat transfer characteristics.
  Experimental methods.
  Numerical methods (simulations).
Preventive maintenance:
  Lubrication
  Checking for misalignments
  Tightening of nut and bolts in manufacturing plants.
Plant shut-down maintenance:
  Collaborations with other teams.
  Precautions for the future.

## Slide 12
Thank you for a wonderful term!